## Slide 1: MCU Based COMPHY28G PHY
Central Engineering Group

## Slide 2: CONTENTS
Firmware Top Level
  Block Diagram
  Flow Chart
  MCU Status
  Memory
  Sequence
Calibration
  Block Diagram
  Related Registers
Power Management
  PCIe PM Diagram
  PCIe PM Controls
  SAS/SATA PM Controls
Training
  Block Diagram
  Flow Chart
  Timing Diagram
  Related Registers
COMMAND IF
  IF Signals
  APTA Command Table
  Tx Command Table
  Rx Command Table
  Cal Command Table

## Slide 3: TOP LEVEL

## Slide 4: FIRMWARE TOP LEVEL – BLOCK DIAGRAM
FIRMWARE
Power Management
Calibration
Tx / Rx Training
Train Interface
Speed Change
Timer / UART
Analog Registers
Digital Registers
CPU
GPIO PINS
UART Tx/Rx

## Slide 5: FIRMWARE TOP LEVEL – FLOW CHART
Initialization
Power-up
MCU START
Speed Change
PLL READY
Rx Init
TRX TRAIN
Real phase adaptation
Check EOM
Calibration Continuous Mode
Rx init triggered
YES
Initialized ?
Calibration
NO
Normal tracking mode
Power State Change
Power saving mode
detected
INTERRUPT service routine when
power state change / speed change detected
Check Status
Power-up calibration detected
Speed change detected
APTA Training
Command Interface

## Slide 6: FIRMWARE TOP LEVEL – INTERRUPT (1) - INTERNAL
Interrupt Signal Name | DIR | Description
int_pu_ivref_chg_isr_lane | I | Interrupt to indicate PIN_PU_IVREF change.
int_pu_pll_chg_isr_lane | I | Interrupt to indicate PIN_PU_PLL change.
int_pu_tx_chg_isr_lane | I | Interrupt to indicate PIN_PU_TX change.
int_pu_rx_chg_isr_lane | I | Interrupt to indicate PIN_PU_RX change.
int_power_state_valid_rise_isr_lane | I | Interrupt to indicate dphy_ana_power_state_valid change for PCIe mode.
int_rx_init_rise_isr_lane | I | Interrupt to indicate PIN_RX_INIT change.
int_refclk_dis_chg_isr_lane | I | Interrupt to indicate PIN_REFCLK_DIS change.
int_pu_pll_or_chg_isr_lane | I | Signal PU_PLL_OR is the OR function output of all pu_pll signals from all lanes.
int_txdetrx_en_chg_isr_lane | I | Interrupt to indicate PIN_TXDETRX_EN change.
int_tx_vcmhold_en_chg_isr_lane | I | Interrupt to indicate PIN_TX_VCMHOLD_EN change. NOT IN USE
int_tx_idle_chg_isr_lane | I | Interrupt to indicate PIN_TX_IDLE change. NOT IN USE
int_pu_sq_chg_isr_lane | I | Interrupt to indicate PIN_PU_SQ change. NOT IN USE
int_tx_idle_hiz_chg_isr_lane | I | Interrupt to indicate PIN_TX_IDLE_HIZ change. NOT IN USE
There are 36 interrupt signals, and 13 of them are not in use.

## Slide 7: FIRMWARE TOP LEVEL – INTERRUPT (2) - INTERNAL
Interrupt Signal Name | DIR | Description
int_beacon_tx_en_chg_isr_lane | I | Interrupt to indicate PIN_TX_ACJTAG_EN change.
pin_papta_train_disable_isr_lane | I | PAPTA Train Disable Interrupt to MCU. Indicates PIN_PAPTA_TRAIN_ENABLE is de-asserted in normal mode.
DME_DEC_ERROR_ISR_LANE | I | DME Decoder Error Interrupt. 1'b0: Differential Manchester decoding is correct. 1'b1: There is something wrong with Differential Manchester decoding. NOT IN USE
dme_dec_remote_balance_err_isr_lane | I | To indicate DME decoder has found that TTIU does not have balanced 0 and 1. NOT IN USE
REMOTE_CTRL_VALID_ISR_LANE | I | Remote Control Field Valid Interrupt. 1'b0: There is no new control bits from remote PHY. 1'b1: There is new new status bits from remote PHY.
REMOTE_STATUS_VALID_ISR_LANE | I | Remote PHY Status Field Valid Interrupt. 1'b0: There is no new status bits from remote PHY. 1'b1: There is new new status bits from remote PHY.
pin_papta_train_enable_isr_lane | I | PAPTA Train Enable Interrupt to MCU.
pin_local_ctrl_field_ready_isr_lane | I | Local Control Field Ready Interrupt to MCU. Indicates PIN_LOCAL_CTRL_FIELD_READY is asserted in normal mode, or PIN_REMOTE_CTRL_FIELD_READY is asserted in loop back mode. NOT IN USE

## Slide 8: FIRMWARE TOP LEVEL – INTERRUPT (3) - INTERNAL
Interrupt Signal Name | DIR | Description
pin_tx_train_enable_isr_lane | I | To indicate either PIN_TX_TRAIN_ENABLE or TX_TRAIN_ENABLE_LANE for this lane is asserted.
pin_rx_train_enable_isr_lane | I | To indicate either PIN_RX_TRAIN_ENABLE or register RX_TRAIN_ENABLE_LANE for this lane is asserted.
dphy_ana_lane_disable_isr_lane | I | PIPE dphy_ana_lane_disable Interrupt. NOT IN USE
int_phy_gen_tx_chg_isr_lane | I | Tx Speed Change Interrupt. Interrupt to indicate PIN_PHY_GEN_TX change. In isolation mode, this interrupt is triggered by register phy_gen_tx_lane[3:0].
int_phy_gen_rx_chg_isr_lane | I | Rx Speed Change Interrupt. Interrupt to indicate PIN_PHY_GEN_RX change. In isolation mode, this interrupt is triggered by register phy_gen_rx_lane[3:0].
frame_lock_isr_lane | I | Frame Lock Interrupt to MCU. This bit indicates frame marker lock after detecting GOOD_MARKER_NUM_LANE of frame marker.
frame_unlock_isr_lane | I | Frame Unlock Interrupt to MCU. This bit indicates frame marker lock after detecting BAD_MARKER_NUM_LANE of frame marker.
lane_margin_en_isr_lane | I | Lane Margin Enable Interrupt To MCU. To indicate PIPE sends out lane margin enable signal. NOT IN USE
phy_mcu_remote_ack_isr_lane | I | PHY MCU Remote Acknowledge Interrupt. Used in command interface. NOT IN USE
phy_mcu_remote_req_isr_lane | I | PHY MCU Remote Request Interrupt. Used in command interface.

## Slide 9: FIRMWARE TOP LEVEL – INTERRUPT (4) - INTERNAL
Interrupt Signal Name | DIR | Description
int_mem_ecc_error_isr_lane | I | Memory ECC Error IRQ. NOT IN USE
int_timer3_isr_lane | I | Timer3 IRQ ISR
int_timer2_isr_lane | I | Timer2 IRQ ISR. NOT IN USE
int_timer1_isr_lane | I | Timer1 IRQ ISR. NOT IN USE
int_timer0_isr_lane | I | Timer0 IRQ ISR. NOT IN USE

## Slide 10: FIRMWARE TOP LEVEL – MCU STATUS - INTERNAL
ST_INIT
0x01
ST_OOR
ST_OOR
ST_RXALIGN90_CAL
ST_P2_BEACON
ST_OOR
ST_POSEQ
ST_RXALIGN90CMP_CAL
ST_TXDETRX
ST_OOR
ST_CAL
ST_RXDCC_EOM_CAL
ST_P2_TXDETRX
ST_OOR
ST_PROCESS_CAL
ST_EOM_ALIGN_CAL
ST_P2
ST_OOR
0x05
ST_PLL_CAL
ST_SAMPLER_CAL
ST_P1
ST_OOR
0x06
ST_PLLDCC_CAL
ST_SQ_CAL
ST_P1_WK
ST_OOR
0x07
ST_VDD_CAL
ST_TXDCC_CAL
ST_P1OFF_WK
ST_OOR
0x08
ST_RXDCC_DLL_CAL
ST_TXDETECT_CAL
ST_P1SNOOZE_WK
ST_OOR
0x09
ST_DLL_COMP_CAL
ST_RXIMP_CAL
ST_P1CLKREQ_WK
ST_OOR
0x0A
ST_DLL_GM_CAL
ST_TXIMP_CAL
ST_PLLREADY
ST_OOR
0x0B
ST_DLL_VDDA_CAL
ST_SPDCHG
ST_TRXTRAIN
ST_OOR
ST_DLL_EOM_GM_CAL
ST_SLUMBER
ST_TXTRAIN
ST_OOR
0x0D
ST_DLL_EOM_VDDA_CAL
ST_P2_WK
ST_RXTRAIN
0x0E
ST_RXDCC_DATA_CAL
ST_PSLUMBER_TX
ST_PSLUMBER_RX
ST_OOR
ST_NORMAL
ST_OOR
ST_DTL
ST_OOR
ST_EOM
ST_OOR
ST_POFF_TXDETRX
ST_OOR
ST_SLUMBER_WK
ST_OOR
ST_SLUMBER_CLK
ST_OOR
ST_PLLTEMP_CAL
ST_OOR
ST_P2_P0
ST_OOR
ST_P1_TXDETRX
ST_OOR
ST_RXALIGN90_TRACK
ST_OOR
ST_PLLAMP_CAL_CONT
ST_OOR
ST_PLL_CAL_RING_CAL
ST_OOR
ST_PLL_PU
ST_OOR
ST_APTA_TXTRAIN
ST_OOR
ST_TXDCC_PDIV_CAL
ST_OOR
ST_RING_PLL_CONT
ST_OOR
ST_LANE_MARGIN_EN
0x0C
0x04
0x03
0x02
0x01
0x00
0x14
0x15
0x16
0x17
0x18
0x19
0x1A
0x1C
0x1D
0x1B
0x13
0x12
0x11
0x10
0x0F
0x23
0x24
0x25
0x26
0x27
0x28
0x29
0x2B
0x2C
0x2A
0x22
0x21
0x20
0x1F
0x1E
0x32
0x33
0x34
0x35
0x36
0x37
0x38
0x3A
0x3B
0x39
0x31
0x30
0x2F
0x2E
0x2D

## Slide 11: FIRMWARE TOP LEVEL – MEMORY INTERNAL
PRAM 64K Byte
ROM 32K Byte
Common XDATA
PIPE Common REG
Digital Common REG
Analog Common REG
Lane XDATA
PIPE Lane REG
Digital Lane REG
Analog Lane REG
0xFFFF
0xE000
0xC000
0xA000
0x8000
0x6000
0x4000
0x2000
0x0000
Program RAM
BANK0
0x8000
0x0000
Program ROM
BANK3
EMPTY
0x0000
External Program RAM
BANK4
0xFFFF
0x0000
0x8000
XDATA Lane Registers:
0x6000 – 0x7FFF
SpeedBlock: 0x6304 – 0x65F4
XDATA Common:
0xE600 – 0XFFFF
SpeedBlock: 0xE000–0xE5DC
Program RAM
BANK1
0xFFFF
External Program RAM
BANK5
0x8000
STC Example

## Slide 12: FIRMWARE TOP LEVEL – SEQUENCE (User Manual)
PRAM EN
FIRMWARE DOWNLOAD
XDATA DOWNLOAD
PIN_DIRECT_ACCESS_EN=1
Starting address:
PIN_PADDR[16:0] = 0x10000
Configure
PMEM_CHECKSUM_EXP[31:0]
Download
<PHY_MODE>_<REFCLK>_CMN.dat
Firmware download successful
Check
PMEM_CHECKSUM_PASS = 1
Download
<PHY_MODE>_LANE.dat
CHECKSUM_CMN*
CHECKSUM_LANE*
DOWNLOAD COMPLETED
PIN_DIRECT_ACCESS_EN = 0
CHECKSUM_CMN
Configure XDATA_MEM_CHECKSUM_EXP_CMN[31:0]
Check XDATA_MEM_CHECKSUM_PASS_CMN=1
CHECKSUM_LANE
Configure XDATA_MEM_CHECKSUM_EXP_LANE[31:0]
Check XDATA_MEM_CHECKSUM_PASS_LANE=1
*: register dedicated per lane

## Slide 13: FIRMWARE TOP LEVEL – SEQUENCE2 (User Manual)
MONITOR
PIN_PLL_READY_TX*/RX* = 0x1
PROGRAM (1)
Assert
EN_LANE* = 1
Program
PIN_PHY_MODE
PIN_REFCLK_SEL
PIN_REF_FREF_SEL[4:0]
PIN_PHY_GEN_TX/RX
PHY_GEN_MAX
INITIALIZE
To keep PIN_TXP* during PHY initialization:
PIN_TX_IDLE = 0x1
PIN_PU_IVREF = 0x1
PIN_PU_PLL = 0x0
PIN_PU_RX* = 0x0
PIN_PU_TX* = 0x0
PROGRAM (2)
TX/RX_SEL_BITS_LANE
Assert
MCU_EN_LANE* = 1
PIN_PU_PLL = 0x1
PIN_PU_RX* = 0x1
PIN_PU_TX* = 0x1
PROGRAM (3)
PIN_TX_IDLE = 0
NORMAL MODE
Toggle PIN_RX_INIT* 0 -> 1 -> 0
Monitor PIN_RX_INIT_DONE* = 1

## Slide 14: FIRMWARE TOP LEVEL – SEQUENCE in Summary
Power-On Sequence

## Slide 15: CALIBRATION

## Slide 16: CALIBRATION – BLOCK DIAGRAM (1) - INTERNAL
From COMPHY_28G CAL_TOP SPEC

## Slide 17: CALIBRATION – BLOCK DIAGRAM (2) - INTERNAL
From COMPHY_28G CAL_TOP SPEC

## Slide 18: CALIBRATION – BLOCK DIAGRAM
CAL START
Process Cal
PLL Cal
LCPLL
RING PLL
TxDetect Cal
Align90 Cal
EOM Cal
DCC Cal
Squelch Cal
Sampler Cal
Lanes
Impedance Cal
CAL DONE
CONTINUOUS CALIBRATION
PLL Temperature Calibration
PLL Amplitude Calibration
PLL DCC Calibration
Ring PLL Calibration
DLL Calibration
TXDCC/RXDCC Calibration
Align90 Calibration
Tx Timing Detect Calibration
VDD Calibration

## Slide 19: CALIBRATION – RELATED REGISTERS
Process Calibration
Register Name | R/W | Description
process_cal_ext_en | W | Bypass process calibration
ANA_PROCESS_VALUE[3:0] | R/W | Result of process calibration to analog
CAL_PROC_SUBSS[7:0] | W | Process Threshold SUBSS[4:0].
CAL_PROC_SS2TT[7:0] | W | Process Threshold SS2TT[4:0].
CAL_PROC_TT2FF[7:0] | W | Process Threshold TT2FF[4:0].
process_cal_done | R | Calibration done flag
process_cal_pass | R | Calibration pass flag
Impedance Calibration
Register Name | R/W | Description
tximp_cal_ext_en | W | Bypass Tx impedance calibration
rximp_cal_ext_en | W | Bypass Rx impedance calibration
vth_tximpcal[2:0] | W | Tx impedance threshold value
vth_rximpcal[2:0] | W | Rx impedance threshold value
IMPCAL_RX_LANE[4:0] | R/W | Rx impedance calibration result for different lanes
cal_tximp_tunep0_lane[7:0] | R/W | Tx impedance calibration result for PMOS side. Thermal code
cal_tximp_tunep_lane[7:0] | R/W | Tx impedance calibration result for PMOS side.
cal_tximp_tunen0_lane[7:0] | R/W | Tx impedance calibration result for NMOS side. Thermal code
cal_tximp_tunen_lane[7:0] | R/W | Tx impedance cal result for NMOS side.
ana_cmn_impcal_out_rd | R | Analog ANA_CMN_IMPCAL_OUT
rximp_cal_done_lane | R | Rx Impedance Calibration Done.
tximp_cal_done_lane | R | Tx Impedance Calibration Done.
rximp_cal_pass_lane | R | Rx Impedance Calibration Pass Indicator.
tximp_cal_pass_lane | R | Tx Impedance Calibration Pass Indicator.
Black: firmware registers
Orange: digital registers
Blue: analog registers

## Slide 20: CALIBRATION – RELATED REGISTERS
20
PLL Calibration
Register Name | R/W | Description
pll_temp_cal_ext_en | W | Bypass PLL temperature calibration
pll_cal_ext_en | W | Bypass PLL calibration
plldcc_cal_ext_en | W | Bypass PLL DCC calibration
ring_pll_cal_ext_en | W | Bypass Ring PLL calibration
pll_temp_cal_cont_en | W | PLL Temperature calibration continuous enable
pllamp_cal_cont_en | W | PLL AMP calibration continuous mode enable.
plldcc_cal_cont_en | W | PLL DCC calibration continuous mode enable.
PLL_SPEED_RING[4:0] | R/W | Ring PLL speed selection
PLL_SLLP_DAC_COARSE_RING[3:0] | R/W | Control VDDVCO coarse tuning
PLL_SLLP_DAC_FINE_RING[10:0] | R/W | Control VDDVCO fine tuning
lcvco_dac_msb[2:0] | R/W | MSB of VCO swing amplitude. Higher value means larger amplitude.
lcvco_dac_lsb[4:0] | R/W | 
lccap_usb | R/W | Control the capacitance of LC tank  VCO frequency
lccap_msb[3:0] | R/W | 
lccap_lsb[4:0] | R/W | 
tempc_dac_sel[7:0] | R/W | Tempc DAC selection
tempc_mux_sel[3:0] | R/W | Tempc mux selection
tempc_mux_hold_sel[3:0] | R/W | Tempc hold selection
20
PLL Calibration
Register Name | R/W | Description
pll_refdiv_ring[3:0] | W | PLL reference divider dividing ratio. Ring PLL reference clock divider ratio.
refdiv[3:0] | W | 
pll_fbdiv_ring[9:8] | W | Control the feedback clock frequency
fbdiv[9:0] | W | 
pll_lpf_r1_sel_ring[2:0] | W | Resistor of low-pass filter
pll_lpfr[1:0] | W | 
icp_ring[3:0] | W | Control the charge pump current
icp_lc[4:0] | W | 
ANA_FBCK_SEL_RING | W | Choose whether the signal before or after PI will go FBDIV. Setting to 0 means PI OFF, FBDIV needs to be set as 4 times as when it’s set to 1
ANA_FBCK_SEL | W | 
pll_amp_cal_done | R | Calibration done flag
pll_temp_cal_done | R | Calibration done flag
pll_cal_done | R | PLL calibration is done
plldcc_cal_done | R | PLL DCC calibration is done
pll_cal_ring_done | R | Ring PLL calibration is done
pll_cal_ring_pass | R | RING PLL Calibration Pass Indicator.
plldcc_cal_pass | R | PLL DCC calibration pass indicator.
pll_amp_cal_pass | R | PLL amplitude calibration pass indicator.
pll_temp_cal_pass | R | PLL temperature calibration pass indicator.
pll_cal_pass | R | PLL calibration pass indicator.

## Slide 21: CALIBRATION – RELATED REGISTERS
Tx DCC Calibration
Register Name | R/W | Description
txdcc_cal_ext_en | W | Bypass TxDCC calibration
txdcc_pdiv_cal_ext_en | W | Bypass TxDCC post divider calibration
txdcc_cnt_lane[5:0] | R/W | Correction code in binary code format. Bit[5] is sign bit. If bit[5]=1, the value is positive.
txdcccal_pdiv_cnt_lane[5:0] | R/W | Tx post divider correction code in binary code format.
txdcc_cal_cont_en | W | Tx DCC Calibration Continuous Enable
txdcc_pdiv_cal_cont_en | W | Tx DCC Post Divider Calibration Continuous Enable
ana_trx_txdcc_dn_rd_lane | R | DCC DN flag signal indicating duty cycle, shared for TX E2C/DCC and post divider DCC. 0: duty cycle<50% 1: duty cycle>50%
txdcc_pdiv_cal_done_lane | R | Tx DCC Post Divider calibration done indicator.
txdcc_cal_done_lane | R | Tx DCC calibration done indicator.
txdcc_pdiv_cal_pass_lane | R | TXDCC post divider calibration pass indicator.
txdcc_cal_pass_lane | R | Tx DCC calibration pass indicator.
Rx DCC Calibration
Register Name | DIR | Description
rxdcc_eom_cal_ext_en | W | Bypass RxDCC EOM calibration
rxdcc_data_cal_ext_en | W | Bypass RxDCC data calibration
rxdcc_dll_cal_ext_en | W | Bypass RxDCC DLL calibration
rxdcc_eomclk_lane[5:0] | R/W | Rx EOM clock DCC code in binary format. Bit[5] is sign bit. If bit[5]=1, the value is positive.
rxdcc_dllclk_lane[5:0] | R/W | Rx DLL Input clock DCC code in binary format. Bit[5] is sign bit. If bit[5]=1, the value is positive.
rxdcc_dataclk_lane[5:0] | R/W | Rx DATA clock DCC code in binary code format. Bit[5] is sign bit. If bit[5]=1, the value is positive.
rxdcc_dll_cal_cont_en | W | Rx DCC Center Calibration Continuous Enable
rxdcc_data_cal_cont_en | W | Rx DCC Center Calibration Continuous Enable
rxdcc_eom_cal_cont_en | W | Rx DCC EOM Calibration Continuous Enable
ana_trx_txdcc_dn_rd_lane | R | flag signal indicating duty cycle 0: duty cycle<50% 1: duty cycle>50%
rxdcc_eom_cal_done_lane | R | RX DCC EOM Calibration Done.
rxdcc_data_cal_done_lane | R | Rx DCC Center Calibration Done.
rxdcc_dll_cal_done_lane | R | RX DCC DLL Calibration Done.
rxdcc_eom_cal_pass_lane | R | Rx DCC EOM Calibration Pass Indicator.
rxdcc_data_cal_pass_lane | R | Rx DCC Center Calibration Pass Indicator.
rxdcc_dll_cal_pass_lane | R | Rx DCC DLL Calibration Pass Indicator.

## Slide 22: CALIBRATION – RELATED REGISTERS
Align90 Calibration
Register Name | R/W | Description
rxalign90_cal_ext_en | W | Bypass Rx align90 calibration
align90_cmp_offset_lane[3:0] | R/W | Comparator offset calibration code. State machine sweep this during the comparator calibration to cancel the inherent offset.
ALIGN90_REF_LANE[5:0] | R/W | Selection for phase shift. Control from the DSP side. ALIGN90_REF will change when align 90 or phase selection happen, ALIGN90_REF is controlled by the DSP side.
align90_gm_lane[2:0] | R/W | Control Gm Strength of Phase Shifter.
align90_dac_lane[5:0] | R/W | Control Gate Bias Voltage of Phase Shifter.
align90_8g_en_lane | W | ALIGN90_8G_EN=0, do not cover 8GHz frequency for align90 delay module, work for PLL freq 10GHz~14GHz ALIGN90_8G_EN=1, align90 delay module work for PLL feq 8GHz~12.5GHz
Align90 Calibration
Register Name | R/W | Description
align90_cal_cont_en | W | Rx Align90 calibration continuous enable
align90_comp_cal_done_lane | R | Align90 comparator calibration done.
rxalign90_cal_done_lane | R | Rx Align90 calibration done.
align90_tracking_pass_lane | R | Rx Align90 phase shifter tracking pass indicator.
align90_comp_pass_lane | R | Rx Align90 comparator calibration pass Indicator.
rxalign90_cal_pass_lane | R | Rx Align90 calibration pass indicator.

## Slide 23: CALIBRATION – RELATED REGISTERS
Squelch Calibration
Register Name | R/W | Description
sq_cal_ext_en | W | Force external cal value
sq_offset_lane[4:0] | R/W | Squelch Offset Calibration Results. This field shows the squelch offset calibration results.
sq_refthr_lane[4:0] | R/W | Squelch Detector Threshold Setting Vpp Single Ended
sq_thresh_lane[5:0] | R/W | SQ Threshold Calibration Results.
PIN_RX_SQ_OUT_RD_LANE | R | Internal Analog Portion Rx Sq Output Read.
sq_cal_done_lane | R | Squelch Calibration Done.
sq_cal_pass_lane | R | Squelch Calibration Pass.
Register Name | R/W | Description
smplr_cal_sel_lane[2:0] | R/W | Selects which sampler to calibrate. Depends on F1 polarity. Set DFE_F1_POL_EN_D/S = 1 000 & F1_POL_D=0 : Calibrate Even Data F1N Sampler 000 & F1_POL_D=1 : Calibrate Even Data F1P Sampler 001 & F1_POL_S=0 : Calibrate Even Slicer F1N Sampler 001 & F1_POL_S=1 : Calibrate Even Slicer F1P Sampler 010: Even Edge Sampler 011 & F1_POL_D=0 : Calibrate Odd Data F1N Sampler 011 & F1_POL_D=1 : Calibrate Odd Data F1P Sampler 100 & F1_POL_S=0 : Calibrate Odd Slicer F1N Sampler 100 & F1_POL_S=1 : Calibrate Odd Slicer F1P Sampler 101: Odd Edge Sampler
Sampler Calibration

## Slide 24: CALIBRATION – RELATED REGISTERS
Sampler Calibration
Register Name | R/W | Description
sampler_cal_ext_en | W | Force external cal value
ofst_f1p_sign_d_e_lane | R/W | Controls offset for even F1P data sampler. Decode from OFST_F1P_D_E[6:0] in digital
ofst_f1p_pos_d_e_lane[4:0] | R/W | Controls offset for even F1P data sampler. Decode from OFST_F1P_D_E[6:0] in digital
ofst_f1p_neg_d_e_lane[4:0] | R/W | Controls offset for even F1P data sampler. Decode from OFST_F1P_D_E[6:0] in digital
ofst_f1n_sign_d_e_lane | R/W | Controls offset for even F1N data sampler. Decode from OFST_F1N_D_E[6:0] in digital
ofst_f1n_pos_d_e_lane[4:0] | R/W | Controls offset for even F1N data sampler. Decode from OFST_F1N_D_E[6:0] in digital
ofst_f1n_neg_d_e_lane[4:0] | R/W | Controls offset for even F1N data sampler. Decode from OFST_F1N_D_E[6:0] in digital
Sampler Calibration
Register Name | R/W | Description
ofst_f1p_sign_d_o_lane | R/W | Controls offset for odd F1P data sampler. Decode from OFST_F1P_D_O[6:0] in digital
ofst_f1p_pos_d_o_lane[4:0] | R/W | Controls offset for odd F1P data sampler. Decode from OFST_F1P_D_O[6:0] in digital
ofst_f1p_neg_d_o_lane[4:0] | R/W | Controls offset for odd F1P data sampler. Decode from OFST_F1P_D_O[6:0] in digital
ofst_f1n_sign_d_o_lane | R/W | Controls offset for odd F1N data sampler. Decode from OFST_F1N_D_O[6:0] in digital
ofst_f1n_pos_d_o_lane[4:0] | R/W | Controls offset for odd F1N data sampler. Decode from OFST_F1N_D_O[6:0] in digital
ofst_f1n_neg_d_o_lane[4:0] | R/W | Controls offset for odd F1N data sampler. Decode from OFST_F1N_D_O[6:0] in digital

## Slide 25: CALIBRATION – RELATED REGISTERS
Sampler Calibration
Register Name | R/W | Description
ofst_f1p_sign_s_e_lane | R/W | Controls offset for even F1P slicer sampler. Decode from OFST_F1P_D_E[6:0] in digital
ofst_f1p_pos_s_e_lane[4:0] | R/W | Controls offset for even F1P slicer sampler. Decode from OFST_F1P_D_E[6:0] in digital
ofst_f1p_neg_s_e_lane[4:0] | R/W | Controls offset for even F1P slicer sampler. Decode from OFST_F1P_D_E[6:0] in digital
ofst_f1n_sign_s_e_lane | R/W | Controls offset for even F1N slicer sampler. Decode from OFST_F1N_D_E[6:0] in digital
ofst_f1n_pos_s_e_lane[4:0] | R/W | Controls offset for even F1N slicer sampler. Decode from OFST_F1N_D_E[6:0] in digital
ofst_f1n_neg_s_e_lane[4:0] | R/W | Controls offset for even F1N slicer sampler. Decode from OFST_F1N_D_E[6:0] in digital
Sampler Calibration
Register Name | R/W | Description
ofst_f1p_sign_s_o_lane | R/W | Controls offset for odd F1P slicer sampler. Decode from OFST_F1P_D_O[6:0] in digital
ofst_f1p_pos_s_o_lane[4:0] | R/W | Controls offset for odd F1P slicer sampler. Decode from OFST_F1P_D_O[6:0] in digital
ofst_f1p_neg_s_o_lane[4:0] | R/W | Controls offset for odd F1P slicer sampler. Decode from OFST_F1P_D_O[6:0] in digital
ofst_f1n_sign_s_o_lane | R/W | Controls offset for odd F1N slicer sampler. Decode from OFST_F1N_D_O[6:0] in digital
ofst_f1n_pos_s_o_lane[4:0] | R/W | Controls offset for odd F1N slicer sampler. Decode from OFST_F1N_D_O[6:0] in digital
ofst_f1n_neg_s_o_lane[4:0] | R/W | Controls offset for odd F1N slicer sampler. Decode from OFST_F1N_D_O[6:0] in digital

## Slide 26: CALIBRATION – RELATED REGISTERS
Sampler Calibration
Register Name | R/W | Description
ofst_edge_sign_e_lane | R/W | Controls offset for even edge sampler. Decode from OFST_EDGE_E[6:0] in digital
ofst_edge_pos_e_lane[4:0] | R/W | Controls offset for even edge sampler. Decode from OFST_EDGE_E [6:0] in digital
ofst_edge_neg_e_lane[4:0] | R/W | Controls offset for even edge sampler. Decode from OFST_EDGE_E6:0] in digital
ofst_edge_sign_o_lane | R/W | Controls offset for odd edge sampler. Decode from OFST_EDGE_O[6:0] in digital
ofst_edge_pos_o_lane[4:0] | R/W | Controls offset for odd edge sampler. Decode from OFST_EDGE_O[6:0] in digital
ofst_edge_neg_o_lane[4:0] | R/W | Controls offset for odd edge sampler. Decode from OFST_EDGE_O[6:0] in digital
Sampler Calibration
Register Name | R/W | Description
ofst_res_lane[1:0] | R/W | Changes the sampler offset resolution per step 00: 2mV 01: 2.5mV 10: 3mV 11: 4mV
sampler_res_cal_done_lane | R | Sampler resolution calibration done.
sampler_cal_done_lane | R | Sampler calibration done.
sampler_cal_pass_lane | R | Sampler Calibration Pass Indicator.

## Slide 27: CALIBRATION – RELATED REGISTERS
DLL Calibration
Register Name | R/W | Description
eom_dll_cal_ext_en | W | Bypass EOM DLL calibration
rxdll_cal_ext_en | W | Bypass Rx DLL calibration
dll_cmp_offset_lane[3:0] | R/W | DAC Current Control. This field controls the strength of the DAC current to compensate for the DLL Comparator offset.
dll_freq_sel_lane[2:0] | R/W | From the speed table, 111: 16GHz 110: 14GHz 110: 12.5GHz 100: 10.3GHz 000: 8GHz
dll_gmsel_lane[2:0] | R/W | Transconductance (Gm) Strength Control of DLL.
SELLV_RXDLL_CH0/1/2/3[5:0] | R/W | Voltage Reference for Slave Regulator of Rx DLL Channel 0/1/2/3.
SELLV_RXEOMDLL_CH0/1/2/3[5:0] | R/W | Voltage Reference for Slave Regulator of Rx EOM DLL Channel 0/1/2/3.
DLL Calibration
Register Name | R/W | Description
eom_dll_cal_cont_en | W | EOM DLL continuous calibration enable
rxdll_cal_cont_en | W | Rx DLL continuous calibration enable
vref_vddadll_half_sel[3:0] | W | Reference voltage that is half of the DLL supply voltage , used to calibrate Gm with the temperature input: 4'b0000 --> 360mV 4'b0001 --> 370mV ... 4'b1110 --> 500mV 4'b1111 --> 510mV
dll_eom_vdata_cal_done_lane | R | DLL EOM VDATA calibration done.
dll_eom_gm_cal_done_lane | R | DLL EOM Gm calibration done.
dll_vdata_cal_done_lane | R | DLL VDATA calibration done.
dll_gm_cal_done_lane | R | DLL Gm calibration done.
dll_comp_cal_done_lane | R | DLL comparator calibration done.
dll_eom_vdata_cal_pass_lane | R | DLL EOM VDATA calibration pass indicator.
dll_eom_gm_cal_pass_lane | R | DLL EOM Gm calibration pass indicator.
dll_vdata_cal_pass_lane | R | DLL VDATA calibration pass indicator.
dll_gm_cal_pass_lane | R | DLL Gm calibration pass indicator.
dll_comp_cal_pass_lane | R | DLL Comparator calibration pass indicator.

## Slide 28: CALIBRATION – RELATED REGISTERS
VDD Calibration
Register Name | R/W | Description
txclk_vdd_cal_ext_en | W | Bypass Tx Clock VDD calibration
txdata_vdd_cal_ext_en | W | Bypass Tx Data VDD calibration
txpre_vdd_cal_ext_en | W | Bypass Tx Pre-Driver VDD calibration
rxdclk_vdd_cal_ext_en | W | Bypass Rx Data Clock VDD calibration
rxeomclk_vdd_cal_ext_en | W | Bypass Rx EOM Clock VDD calibration
rxsmplr_vdd_cal_ext_en | W | Bypass Rx Sampler VDD calibration
vdd_cal_ext_en | W | Bypass VDD calibration
sellv_txclk_ch0/1/2/3[3:0] | R/W | TX clock voltage regulator control value. Unsigned binary
sellv_txdata_ch0/1/2/3[3:0] | R/W | TX data voltage regulator control value. Unsigned binary
sellv_txpre_ch0/1/2/3[3:0] | R/W | TX pre-driver voltage regulator control value. Unsigned binary
sellv_rxeomclk_ch0/1/2/3[3:0] | R/W | RX EOM clock routing voltage regulator control value. Unsigned binary
sellv_rxdataclk_ch0/1/2/3[3:0] | R/W | RX data clock voltage regulator control value. Unsigned binary
sellv_rxsampelr_ch0/1/2/3[3:0] | R/W | RX sampler voltage regulator control value . Unsigned binary
VDD Calibration
Register Name | R/W | Description
vref_vddacal_sel[2:0] | R/W | Voltage Reference for VDDA Calibration:. 3'b000: 440 mV 3'b001: 450 mV 3'b010: 460 mV 3'b011: 470 mV 3'b100: 475 mV 3'b101: 480 mV 3'b110: 490 mV 3'b111: 500 mV
txclk_vdd_cal_cont_en | W | TxClk VDD calibration continuous enable
txdata_vdd_cal_cont_en | W | TxDATA VDD calibration continuous enable
txpre_vdd_cal_cont_en | W | TX Pre-Driver VDD calibration continuous enable
rxdclk_vdd_cal_cont_en | W | Rx data clock VDD calibration continuous enable
rxeomclk_vdd_cal_cont_en | W | Rx EOM clock VDD calibration continuous enable
rxsmplr_vdd_cal_cont_en | W | Rx sampler VDD calibration continuous enable

## Slide 29: CALIBRATION – RELATED REGISTERS
VDD Calibration
Register Name | R/W | Description
vdd_cal_done_lane | R | VDD calibration done indicator.
vdd_cal_pass_lane | R | VDD calibration pass indicator.
sellv_rxsampler_pass_lane | R | VDD Calibration Sellv_Rxsampler pass indicator.
sellv_rxeomclk_pass_lane | R | VDD Calibration Sellv_Rxeomclk Pass Indicator.
sellv_rxdataclk_pass_lane | R | VDD Calibration Sellv_Rxdataclk Pass Indicator.
sellv_rxintp_pass_lane | R | VDD Calibration Sellv_Rxintp Pass Indicator.
sellv_txpre_pass_lane | R | VDD Calibration Sellv_Txpre Pass Indicator.
sellv_txdata_pass_lane | R | VDD Calibration Sellv_Txdata Pass Indicator.
sellv_txclk_pass_lane | R | VDD Calibration Sellv_Txclk Pass Indicator.
TxDetect Calibration
Register Name | R/W | Description
txdetect_cal_ext_en | W | Bypass Tx Timing Detect calibration.
txdetect_cal_cont_en | W | Tx Detect Continuous calibration enable
txdetect_cal_step_size[7:0] | W | TXDETECT Cal Continuous Step Size
sellv_txdata_ch0/1/2/3[3:0] | R/W | TX data voltage regulator control value. Unsigned binary
txdetect_cal_done_lane | R | Tx Timing Detect calibration done.
txdetect_cal_pass_lane | R | Tx Timing Detect calibration pass indicator.
Other Calibration Registers
Register Name | R/W | Description
cal_start | W | Calibration manual start.
force_cont_cal_skip | W | Force continuous calibration to skip.
CAL_DONE | R | Calibration done.
EXT_FORCE_CAL_DONE | R | External force calibration done

## Slide 30: POWER MANAGEMENT

## Slide 31: POWER MANAGEMENT – PCIe Mode - INTERNAL
Power State Flow:
From COMPHY_28G PM SPEC

## Slide 32: POWER MANAGEMENT – PCIe Mode - INTERNAL
P0
Signal Names | Dir | Value
PIN_PU_IVREF | I | 1
PIN_PU_PLL* | I | 1
PIN_PU_RX* | I | 1
PIN_PU_TX* | I | 1
PIN_REFCLK_DIS | I | 0
PIN_TX_IDLE | I | 0
PIN_TX_VCMHOLD_EN | I | 0
PIN_TX_IDLE_HIZ | I | 0
Signal Names | Dir | Value
PIN_TX_VCMHOLD_EN_RD_LANE | O | 0
PIN_TX_IDLE_HIZ_RD_LANE | O | 0
ANA_PU_IVREF | O | 1
ANA_PU_PLL | O | 1
ANA_PU_RX_LANE | O | 1
ANA_PU_TX_LANE | O | 1
PULUP | O | 0
SHRTR | O | 0
ANA_LD_CAL_DATA | O | 0
PLL_CLK_READY | O | 1
DFE_CLK_OFF_LANE | O | 0
Signal Names | Dir | Value
DTL_CLK_OFF_LANE | O | 0
DTX_CLK_OFF | O | 0
RESET_DTX | O | 0
RESET_DTL_LANE | O | 0
RESET_DFE_LANE | O | 0
RESET_ANA | O | 0
PIN_REFCLK_DIS_RD | O | 0
PU_IVREF_FELL | O | 0
PU_BG_FELL | O | 0
CLKCPU_EN_LANE* | O | 1
PIN_PLL_READY_RX* | O | 1
PIN_PLL_READY_TX* | O | 1

## Slide 33: POWER MANAGEMENT – PCIe Mode - INTERNAL
P0s
Signal Names | Dir | Value
PIN_PU_IVREF | I | 1
PIN_PU_PLL* | I | 1
PIN_PU_RX* | I | 1
PIN_PU_TX* | I | 1
PIN_REFCLK_DIS | I | 0
PIN_TX_IDLE | I | 1
PIN_TX_VCMHOLD_EN | I | 0
PIN_TX_IDLE_HIZ | I | 0
Signal Names | Dir | Value
PIN_TX_VCMHOLD_EN_RD_LANE | O | 0
PIN_TX_IDLE_HIZ_RD_LANE | O | 0
ANA_PU_IVREF | O | 1
ANA_PU_PLL | O | 1
ANA_PU_RX_LANE | O | 1
ANA_PU_TX_LANE | O | 1
PULUP | O | 0
SHRTR | O | 0
ANA_LD_CAL_DATA | O | 0
PLL_CLK_READY | O | 1
DFE_CLK_OFF_LANE | O | 0
Signal Names | Dir | Value
DTL_CLK_OFF_LANE | O | 0
DTX_CLK_OFF | O | 0
RESET_DTX | O | 0
RESET_DTL_LANE | O | 0
RESET_DFE_LANE | O | 0
RESET_ANA | O | 0
PIN_REFCLK_DIS_RD | O | 0
PU_IVREF_FELL | O | 0
PU_BG_FELL | O | 0
CLKCPU_EN_LANE* | O | 1
PIN_PLL_READY_RX* | O | 1
PIN_PLL_READY_TX* | O | 1

## Slide 34: POWER MANAGEMENT – PCIe Mode - INTERNAL
P1
Signal Names | Dir | Value
PIN_PU_IVREF | I | 1
PIN_PU_PLL* | I | 1
PIN_PU_RX* | I | 0
PIN_PU_TX* | I | 1
PIN_REFCLK_DIS | I | 0
PIN_TX_IDLE | I | 1
PIN_TX_VCMHOLD_EN | I | 0
PIN_TX_IDLE_HIZ | I | 1
Signal Names | Dir | Value
PIN_TX_VCMHOLD_EN_RD_LANE | O | 0
PIN_TX_IDLE_HIZ_RD_LANE | O | 1
TX_LESS_CUR_IDLE (lane0) | O | 1
ANA_PU_IVREF | O | 1
ANA_PU_PLL | O | 1
ANA_PU_RX_LANE | O | 0
ANA_PU_TX_LANE | O | 1
PULUP | O | 0
SHRTR | O | 0
ANA_LD_CAL_DATA | O | 0
PLL_CLK_READY | O | 1
DFE_CLK_OFF_LANE | O | 1
Signal Names | Dir | Value
DTL_CLK_OFF_LANE | O | 1
DTX_CLK_OFF | O | 0
RESET_DTX | O | 0
RESET_DTL_LANE | O | 1
RESET_DFE_LANE | O | 1
RESET_ANA | O | 0
PIN_REFCLK_DIS_RD | O | 0
PU_IVREF_FELL | O | 0
PU_BG_FELL | O | 0
CLKCPU_EN_LANE* | O | 1
PIN_PLL_READY_RX* | O | 0
PIN_PLL_READY_TX* | O | 1

## Slide 35: POWER MANAGEMENT – PCIe Mode- INTERNAL
P1.CLKREQ
Signal Names | Dir | Value
PIN_PU_IVREF | I | 1
PIN_PU_PLL* | I | 0
PIN_PU_RX* | I | 0
PIN_PU_TX* | I | 0
PIN_REFCLK_DIS | I | 1
PIN_TX_IDLE | I | 1
PIN_TX_VCMHOLD_EN | I | 1
PIN_TX_IDLE_HIZ | I | 1
Signal Names | Dir | Value
PIN_TX_VCMHOLD_EN_RD_LANE | O | 1
PIN_TX_IDLE_HIZ_RD_LANE | O | 1
TX_LESS_CUR_IDLE (lane0) | O | 1
ANA_PU_IVREF | O | 1
ANA_PU_PLL | O | 0
ANA_PU_RX_LANE | O | 0
ANA_PU_TX_LANE | O | 0
PULUP | O | 0
SHRTR | O | 0
ANA_LD_CAL_DATA | O | 0
PLL_CLK_READY | O | 0
DFE_CLK_OFF_LANE | O | 1
Signal Names | Dir | Value
DTL_CLK_OFF_LANE | O | 1
DTX_CLK_OFF | O | 1
RESET_DTX | O | 1
RESET_DTL_LANE | O | 1
RESET_DFE_LANE | O | 1
RESET_ANA | O | 1
PIN_REFCLK_DIS_RD | O | 1
PU_IVREF_FELL | O | 0
PU_BG_FELL | O | 0
CLKCPU_EN_LANE* | O | 0
PIN_PLL_READY_RX* | O | 0
PIN_PLL_READY_TX* | O | 0

## Slide 36: POWER MANAGEMENT – PCIe Mode - INTERNAL
P1.SNOOZE
Signal Names | Dir | Value
PIN_PU_IVREF | I | 0
PIN_PU_PLL* | I | 0
PIN_PU_RX* | I | 0
PIN_PU_TX* | I | 0
PIN_REFCLK_DIS | I | 1
PIN_TX_IDLE | I | 1
PIN_TX_VCMHOLD_EN | I | 1
PIN_TX_IDLE_HIZ | I | 1
Signal Names | Dir | Value
PIN_TX_VCMHOLD_EN_RD_LANE | O | 1
PIN_TX_IDLE_HIZ_RD_LANE | O | 1
TX_LESS_CUR_IDLE (lane0) | O | 1
ANA_PU_IVREF | O | 0
ANA_PU_PLL | O | 0
ANA_PU_RX_LANE | O | 0
ANA_PU_TX_LANE | O | 0
PULUP | O | 0
SHRTR | O | 0
ANA_LD_CAL_DATA | O | 0
PLL_CLK_READY | O | 0
DFE_CLK_OFF_LANE | O | 1
Signal Names | Dir | Value
DTL_CLK_OFF_LANE | O | 1
DTX_CLK_OFF | O | 1
RESET_DTX | O | 1
RESET_DTL_LANE | O | 1
RESET_DFE_LANE | O | 1
RESET_ANA | O | 1
PIN_REFCLK_DIS_RD | O | 1
PU_IVREF_FELL | O | 1
PU_BG_FELL | O | 0
CLKCPU_EN_LANE* | O | 0
PIN_PLL_READY_RX* | O | 0
PIN_PLL_READY_TX* | O | 0

## Slide 37: POWER MANAGEMENT – PCIe Mode - INTERNAL
P1.OFF
Signal Names | Dir | Value
PIN_PU_IVREF | I | 0
PIN_PU_PLL* | I | 0
PIN_PU_RX* | I | 0
PIN_PU_TX* | I | 0
PIN_REFCLK_DIS | I | 1
PIN_TX_IDLE | I | 1
PIN_TX_VCMHOLD_EN | I | 0
PIN_TX_IDLE_HIZ | I | 0
Signal Names | Dir | Value
PIN_TX_VCMHOLD_EN_RD_LANE | O | 0
PIN_TX_IDLE_HIZ_RD_LANE | O | 0
TX_LESS_CUR_IDLE (lane0) | O | 0
ANA_PU_IVREF | O | 0
ANA_PU_PLL | O | 0
ANA_PU_RX_LANE | O | 0
ANA_PU_TX_LANE | O | 0
PULUP | O | 0
SHRTR | O | 0
ANA_LD_CAL_DATA | O | 0
PLL_CLK_READY | O | 0
DFE_CLK_OFF_LANE | O | 1
Signal Names | Dir | Value
DTL_CLK_OFF_LANE | O | 1
DTX_CLK_OFF | O | 1
RESET_DTX | O | 1
RESET_DTL_LANE | O | 1
RESET_DFE_LANE | O | 1
RESET_ANA | O | 1
PIN_REFCLK_DIS_RD | O | 1
PU_IVREF_FELL | O | 1
PU_BG_FELL | O | 1
CLKCPU_EN_LANE* | O | 0
PIN_PLL_READY_RX* | O | 0
PIN_PLL_READY_TX* | O | 0

## Slide 38: POWER MANAGEMENT – PCIe Mode - INTERNAL
P2
Signal Names | Dir | Value
PIN_PU_IVREF | I | 1
PIN_PU_PLL* | I | 0
PIN_PU_RX* | I | 0
PIN_PU_TX* | I | 0
PIN_REFCLK_DIS | I | 0
PIN_TX_IDLE | I | 1
PIN_TX_VCMHOLD_EN | I | 1
PIN_TX_IDLE_HIZ | I | 1
Signal Names | Dir | Value
PIN_TX_VCMHOLD_EN_RD_LANE | O | 1
PIN_TX_IDLE_HIZ_RD_LANE | O | 1
TX_LESS_CUR_IDLE (lane0) | O | 1
ANA_PU_IVREF | O | 1
ANA_PU_PLL | O | 0
ANA_PU_RX_LANE | O | 0
ANA_PU_TX_LANE | O | 0
PULUP | O | 0
SHRTR | O | 0
ANA_LD_CAL_DATA | O | 0
PLL_CLK_READY | O | 0
DFE_CLK_OFF_LANE | O | 1
Signal Names | Dir | Value
DTL_CLK_OFF_LANE | O | 1
DTX_CLK_OFF | O | 1
RESET_DTX | O | 1
RESET_DTL_LANE | O | 1
RESET_DFE_LANE | O | 1
RESET_ANA | O | 1
PIN_REFCLK_DIS_RD | O | 0
PU_IVREF_FELL | O | 0
PU_BG_FELL | O | 0
CLKCPU_EN_LANE* | O | 1
PIN_PLL_READY_RX* | O | 0
PIN_PLL_READY_TX* | O | 0

## Slide 39: POWER MANAGEMENT – PCIe Mode - INTERNAL
P0 / P0s to Beacon
P2 to Beacon
Signal Names | Dir | Value
PIN_TX_ACJTAG_EN | I | 1
Signal Names | Dir | Value
ANA_BEACON_EN_LANE (lane0) | O | 1
Signal Names | Dir | Value
ANA_PU_TX_LANE (lane0) | O | 1
PIN_TX_IDLE_HIZ_RD_LANE | O | 0
TX_LESS_CUR_IDLE (lane0) | O | 0
ANA_BEACON_EN_LANE (lane0) | O | 1
Signal Names | Dir | Value
PIN_TX_ACJTAG_EN | I | 1

## Slide 40: POWER MANAGEMENT – PCIe/USB Mode
Power State Control
Power States (PCIE/USB3) | PU_PLL | PU_TX | PU_RX | IDLE | TX_IDLE_HIZ_EN_LESS_CUR_IDLE | PU_IVREF | PU_BG | PU_SQ | REFCLK | MCU CLK
P0/P0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 1 | ON | ON
P0s/P1 | 1 | 1 | 1 | 1 | 0 | 1 | 1 | 1 | ON | ON
P1/P2 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1 | ON | ON
P2/P3 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | OFF | ON
P1.CLKREQ/ | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | OFF | OFF
P1.SNOOZE/ | 0 | 0 | 0 | 1 | 1 | 0 | 1 | 0 | OFF | OFF
P1.OFF/ | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | OFF | OFF

## Slide 41: POWER MANAGEMENT – SAS/SATA Mode
Power State Control
Power States | PIN_PU_IVREF | PIN_PU_PLL | PIN_PU_TX | PIN_PU_RX | PIN_REFCLK_DIS
All On | 1 | 1 | 1 | 1 | 0
Rx Partial | 1 | 1 | 1 | 0 | 0
Tx Partial | 1 | 1 | 0 | 1 | 0
Rx/Tx Partial | 1 | 1 | 0 | 0 | 0
Slumber | 1 | 0 | 0 | 0 | 0
Slumber Clock Off | 1 | 0 | 0 | 0 | 1
Slumber IVREF Off | 0 | 0 | 0 | 0 | 0
Slumber Clock Off & IVREF Off | 0 | 0 | 0 | 0 | 1

## Slide 42: TRAINING

## Slide 43: TRAINING – BLOCK DIAGRAM
TRX TRAINING
STATE MACHINE

## Slide 44: TRAINING – FW FLOW CHART
Training Bypass
Register Name | R/W | Description
bypass_rxtrain_lane | W | Force Bypass Rx Train during TRx Train for Test.
bypass_ctle_train_lane | W | Bypass Rx CTLE Train for Test.
CDRPHASE_OPT_EN_LANE | W | 0: Bypass Rx Phase train for Test.
gain_train_init_en_lane | W | GAIN TRAIN: 0: DFE resolution training disable during Tx/Rx train initialize state.
gain_train_end_en_lane | W | GAIN TRAIN: 0: DFE resolution training disable during Tx/Rx train end state.

## Slide 45: TRAINING – FW FLOW CHART - INTERNAL
Tx Training
Rx Training

## Slide 46: TRAINING TIMING DIAGRAM
Training Timer
Register Name | Default | R/W | Description
tx_train_status_det_timer_enable_lane | 1’b1 | W | Tx Train Status Detection Timeout Enable.
RX_TRAIN_TIMER_ENABLE_LANE | 1’b1 | W | Rx Train Timeout Enable.
TX_TRAIN_TIMER_ENABLE_LANE | 1’b1 | W | Tx Train Timeout Enable.
TX_TRAIN_FRAME_DET_TIMER_ENABLE_LANE | 1’b1 | W | Tx Train Frame Detection Timeout Enable.
frame_lock_sel_timeout_lane | 1’b0 | W | Frame Lock Select Timeout. 1'b0: Use internal generated frame lock signal to start TRx train frame detection timers. 1'b1: Use PIN_TX_TRAIN_ENABLE as frame lock to start TRx train frame detection timers.
tx_train_status_det_timeout_int_lane | 1’b0 | R | Tx Train Status Detect Timeout Indicator from MCU.

## Slide 47: TRAINING – TRX FLOW CHART - INTERNAL
TRX Training Initial State
TRX Training Initial State Start
Reset parameters & variables in TRX training
Rx_No_Init?
Set Rx-FFE to the init setting
DFE & CDR Phase Opt State
Tx_train_en && !Tx_No_Init?
Reset Tx-FFE
GAIN_TRAIN_INIT_EN_LANE ?
DFE & CDR Phase Opt State
Save train memory to opt memory
CDRPHASE_OPT_EN_LANE ?
Set train R, train C to
reg_rxffe_R_gain_train
reg_rxffe_C_gain_train
CDRPHASE_OPT_EN <= 0
Gain Training
Set FFE_R & FFE_C
back to init
Call DFE&CDR Optimization
Save train memory to opt memory
TRX Training Initial State End
NO
YES
NO
YES
DFE & CDR Phase Opt State
YES
NO
YES
NO

## Slide 48: TRAINING – TRX FLOW CHART - INTERNAL
TRX Training End State
TRX Training End State Start
GAIN_TRAIN_INIT_EN_LANE ?
Load opt memory to train memory
Gain Training
TRX Training Initial State End
Save train memory to opt memory
NO
YES

## Slide 49: TRAINING – GAIN TRAIN FLOW CHART - INTERNAL
Gain Training Start
step_num <= 0
gain_index <= 0
Gain table size <=
gain_train_with_sampler? (gain_train_with_c? 22:7) : (gain_train_with_c?19:4)
Gain table index <=
gain_train_with_sampler? (gain_train_with_c? 3:2) : (gain_train_with_c?1:0)
step_num < gain_table_size + 1
Set DFE_RES and sampler based on gain mapping table 0/1/2/3 (gain_table_index) and gain_index
Call DFE&CDR optimization state.
step_number ++
gain_index –
(actual gain increases)
Gain Training End
gain_index ++
(actual gain decreases)
f0a < res_f0a_low_thres && dfe_satur_status && gain_index >= 1?
f0a >= (res_f0a_high_thres || (f0a >= res_f0a_low_thres && dfe_saturate)) && (gain_index < gain_table_size – 1)?
NO
YES
NO
YES
YES
NO

## Slide 50: Training Algorithm – Brute-force Search in Tx FFE / CDR
Brute-force search is used to find the maximal eye opening and to optimize CDR phase & Tx G0/Gn1/G1 adaptations.
Algorithm sequence:
  Decrease (increase) index by step_num times; each time decreases (increases) step_size step(s)
  Return to the initial index
  Increase (decrease) index by step_num times; each time increases (decrease) step_size step(s)
step_size = 2, Blue:Decrease, Green:Increase

## Slide 51: Training Algorithm – Midpoint in Tx FFE / CDR
It is recommended to tune these parameters for the stressful conditions such as adding high insertion loss (long cables).
step_size = 2, Blue:Decrease, Green:Increase
Dynamic threshold = k * init_eo + c,
where k and c are coefficients user programs,
init_eo is an internal eye opening measurement
The midpoint algorithm will decrease the index
(in step of step_size) to find the smallest index with
eye open equal or bigger than the threshold.
Such index is called index_small.
Then we return to the initial condition, and increase
the index to find the largest index where eye opening is equal to bigger than the threshold.
This index is called index_large.
The average of the index_small and index_large is the
final trained index. Note, the thresholds used for search index_small and index_large can be set independently, therefore, we have k_small and k_large as well as c_small and c_large.

## Slide 52: Training Algorithm – F0p in CDR
F0p mode
  When maxf0p_mode is selected, CDR phase is adjusted based on Brute-force search where the phase is first decreased and then increased.
Sequence
F0p calculation to be compared with the optimal value
  train_f0p <= eye_check_pass * (eo * f0p_eo_based + f0_minus_abs_fn1 * (!f0p_eo_based)
  ,where if f0 >= f0a
    f0_minus_abs_fn1 <= f0a
    else
    f0_minus_abs_fn1 <= 2*f0 – f0a
Phase Direction Defines
CDR Phase
Maxf0p State Start
Phase Adjustment State
1. phase_offset <= phase_offset + direction*phase_step_size
2. Num_count ++
DFE & CDR Phase Optimization State
Call DFE&CDR phase opt state
Call f0p calculation
Update State
END

## Slide 53: CDR Phase Optimization Scheme - INTERNAL

## Slide 54: CDR Phase Optimization Scheme

## Slide 55: Training Algorithm – FFE Adaptation - INTERNAL
Search Table
  The search table algorithm will choose FFE_RES1, FFE_RES2, FFE_CAP1, and FFE_CAP2 set in the table to find the maximal eye opening F0D. The combinations of FFE_RES and FFE_CAP are built in firmware.
  When Gain_Train_with_C mode is enable, FFE_CAP will not be swept in the search table.
  The search table algorithm has some limits set by below registers.
    RX_FFE_OVERBOOST_THRES_LANE[3:0] : To avoid over boost
    DFE_F0_SAT_THRES_LANE[7:0] : To avoid saturated F0A.
  However, these limits and maximal F0D are disabled when Minimum Boost Mode is enabled by default.

## Slide 56: Training Algorithm – FFE Adaptation
Gain_Train_with_C Mode
  This mode adapts both the DFE_RES and the FFE_CAP at the same time to control the effective gain in the DFE to not saturate.
  FFE_CAP controls CTLE peak gain. Decreasing FFE_CAP could reduce total CTLE gain. A good FFE_CAP setting should provide non-saturated DFE results and use DFE dynamic range as much as possible. Hence, we init FFE_CAP = F (max), and then reduce FFE_CAP until the adapted DFE is not saturated.
  At the initial gain-training at the beginning, the algorithm adapts both the DFE_RESolution and the FFE_CAP, this is used as the starting parameters.
  During FFE training, the
  FFE_CAP can be updated
  depending on if HW gets better
  results. At the last gain-training
  at the end, only DFE_RESolution is
  Is re-adapted.

## Slide 57: Training Algorithm – FFE Adaptation, INTERNAL
Overboost
  Overboost happens when the CTLE overcompensates the channel (e.g. boost gain > insertion loss at Nyquist).
  In order to avoid overboost in medium/short traces a set of overboost criteria are defined.
  i.e.:
    RX-FFE: F1 + F2 < threshold
    RX-FFE: F3 < threshold, RX-FFE: F3 < threshold, RX-FFE: F3 < threshold
In the RX-FFE comparison
    Choose RX-FFE without overboost
    When both RX-FFEs are overboost, choose the one with larger R or smaller C

## Slide 58: DFE ADAPTATION SEQUENCE - INTERNAL
F0A
Coarse Adaptation
DFE
Coarse Adaptation
DFE
Fine Adaptation
DFE
Accurate Adaptation
DFE DC
Fine Adaptation
DFE DC
Accurate Adaptation
F0B
Fine Adaptation
F0B
Accurate Adaptation
F0D
Fine Adaptation
F0D
Coarse Adaptation
Eye Check State

## Slide 59: TRAINING – Related Registers
Tx Train
NAME OF REGISTERS | DIR | DESCRIPTION
TX_G0_STEP_SIZE_LANE[3:0] | W | Tx G0 step size
TX_G1_STEP_SIZE_LANE[1:0] | W | Tx G1 step size
TX_GN1_STEP_SIZE_LANE[1:0] | W | Tx Gn1 step size
TX_G0_STEP_NUM_LANE[3:0] | W | Number of Tx G0 steps to be searched.
TX_G1_STEP_NUM_LANE[4:0] | W | Number of Tx G1 steps to be searched.
TX_GN1_STEP_NUM_LANE[4:0] | W | Number of Tx GN1 steps to be searched.
TX_G1_MAXF0T_EN_LANE | W | Tx G1 Max F0t train enable
TX_GN1_MAXF0T_EN_LANE | W | Tx GN1 Max F0t train enable
TX_G1_MIDPOINT_EN_LANE | W | TX G1 mid-point train enable
TX_GN1_MIDPOINT_EN_LANE | W | TX GN1 mid-point train enable
TX_ADAPT_G0_EN_LANE | W | Tx FFE adapt G0 enable.
TX_ADAPT_GN1_EN_LANE | W | Tx FFE adapt Gn1 enable.
NAME OF REGISTERS | DIR | DESCRIPTION
TX_ADAPT_G1_EN_LANE | W | Tx FFE adapt G1 enable.
tx_gn1_midpoint_thres_k_lane[7:0] | W | Tx Gn1 Midpoint Threshold K
tx_gn1_midpoint_thres_c_lane[7:0] | W | Tx Gn1 Midpoint Threshold C (2's Complement)
tx_g1_midpoint_thres_k_lane[7:0] | W | Tx G1 Midpoint Threshold K
tx_g1_midpoint_thres_c_lane[7:0] | W | Midpoint small threshold c.
local_tx_preset_index[3:0] | W | Local TX Coefficient Preset Index. When TX train begin, local TX will set it's TX coefficient to different preset value. 4'h1: default 1, 4’h2: default 2 … 4’hb: default 11 Other: reserved

## Slide 60: TRAINING – Related Registers
Tx Train
NAME OF REGISTERS | R/W | DESCRIPTION
cfg_cursor_preset0_lane | W | Cursor coefficient of preset0
cfg_cursor_preset1_lane | W | Cursor coefficient of preset1
cfg_cursor_preset2_lane | W | Cursor coefficient of preset2
cfg_cursor_preset3_lane | W | Cursor coefficient of preset3
cfg_cursor_preset4_lane | W | Cursor coefficient of preset4
cfg_cursor_preset5_lane | W | Cursor coefficient of preset5
cfg_cursor_preset6_lane | W | Cursor coefficient of preset6
cfg_cursor_preset7_lane | W | Cursor coefficient of preset7
cfg_cursor_preset8_lane | W | Cursor coefficient of preset8
cfg_cursor_preset9_lane | W | Cursor coefficient of preset9
cfg_cursor_preset10_lane | W | Cursor coefficient of preset10
NAME OF REGISTERS | R/W | DESCRIPTION
cfg_post_cursor_preset0_lane | W | Post-Cursor coefficient of preset0
cfg_post_cursor_preset1_lane | W | Post-Cursor coefficient of preset1
cfg_post_cursor_preset2_lane | W | Post-Cursor coefficient of preset2
cfg_post_cursor_preset3_lane | W | Post-Cursor coefficient of preset3
cfg_post_cursor_preset4_lane | W | Post-Cursor coefficient of preset4
cfg_post_cursor_preset5_lane | W | Post-Cursor coefficient of preset5
cfg_post_cursor_preset6_lane | W | Post-Cursor coefficient of preset6
cfg_post_cursor_preset7_lane | W | Post-Cursor coefficient of preset7
cfg_post_cursor_preset8_lane | W | Post-Cursor coefficient of preset8
cfg_post_cursor_preset9_lane | W | Post-Cursor coefficient of preset9
cfg_post_cursor_preset10_lane | W | Post-Cursor coefficient of preset10

## Slide 61: TRAINING – Related Registers
Name of Registers | R/W | DESCRIPTION
cfg_pre_cursor_preset0_lane | W | Pre-Cursor coefficient of preset0
cfg_pre_cursor_preset1_lane | W | Pre-Cursor coefficient of preset1
cfg_pre_cursor_preset2_lane | W | Pre-Cursor coefficient of preset2
cfg_pre_cursor_preset3_lane | W | Pre-Cursor coefficient of preset3
cfg_pre_cursor_preset4_lane | W | Pre-Cursor coefficient of preset4
cfg_pre_cursor_preset5_lane | W | Pre-Cursor coefficient of preset5
cfg_pre_cursor_preset6_lane | W | Pre-Cursor coefficient of preset6
cfg_pre_cursor_preset7_lane | W | Pre-Cursor coefficient of preset7
cfg_pre_cursor_preset8_lane | W | Pre-Cursor coefficient of preset8
cfg_pre_cursor_preset9_lane | W | Pre-Cursor coefficient of preset9
cfg_pre_cursor_preset10_lane | W | Pre-Cursor coefficient of preset10
Tx Train
Name of Registers | R/W | DESCRIPTION
CFG_EQ_FS_LANE | W | Local transmitter full swing parameter (FS).
CFG_EQ_16G_FS_LANE | W | Local transmitter full swing parameter (FS).
CFG_EQ_LF_LANE | W | Local transmitter low frequency Parameter (LF).
CFG_EQ_16G_LF_LANE | W | Local transmitter low frequency parameter (LF).
cfg_tx_coeff_max0_lane | W | Local Tx transmitter coefficient maximum value. Bit[5:0]: C-1 Bit[11:6]:C0
cfg_tx_coeff_max1_lane | W | Local Tx transmitter coefficient maximum value. Bit[5:0]: C+1
TX_EM_PRE_MAX_LANE[3:0] | W | Tx pre emphasis maximum
TX_EM_PO_MAX_LANE[3:0] | W | Tx post emphasis maximum
TX_EM_PEAK_MIN_LANE[3:0] | W | Tx peak emphasis minimum

## Slide 62: TRAINING – Related Registers
Name of Registers | R/W | DESCRIPTION
TX_EM_PEAK_MAX_LANE[3:0] | W | Tx Peak Emphasis Maximum
TX_TRAIN_P2P_HOLD_LANE | W | Tx train peak to peak hold enable. 1'b0: Tx coefficient control separately. 1'b1: Hold the range of peak to peak range. The coefficient changes of G0, G1 and Gn1 impact each other.
tx_no_init_lane | W | No Tx initial during Tx train. 1’b0: TX preset commands are sent to remote PHY. Which preset command is used is determined by the register tx_preset_index_lane[7:0]. 1’b1: TX preset commands are not sent to remote PHY at the beginning of the TX training.
TRAIN_G0_LANE[7:0] | R/W | Tx Train G0 Value.
TRAIN_G1_LANE[7:0] | R/W | Tx Train G1 Value.
TRAIN_GN1_LANE[7:0] | R/W | Tx Train GN1 Value.
pipe_eq_status_lane | R | PIPE Internal Equalization Status Selection.
Tx Train

## Slide 63: TRAINING – Related Registers
CDR Train
Name of Registers | DIR | Description
CDRPHASE_OPT_EN_LANE | W | 0: CDR phase optimization train bypass 1: CDR phase optimization train enable.
CDR_MAXF0P_EN_LANE | W | CDR max F0p train enable
CDR_MIDPOINT_EN_LANE | W | CDR midpoint train enable
CDR_STEP_NUM_LANE[3:0] | W | CDR step number
midpoint_small_thres_k_lane | W | CDR midpoint small threshold k.
midpoint_small_thres_c_lane | W | CDR midpoint small threshold c.
midpoint_large_thres_k_lane | W | CDR midpoint large threshold k.
midpoint_large_thres_c_lane | W | CDR midpoint large threshold c.

## Slide 64: TRAINING – Related Registers
FFE Train
Name of Registers | DIR | Description
rx_ffe_overboost_thres_lane | W | Rx FFE overboost threshold => To avoid over boost.
sumf_boost_target_k_lane[7:0] | W | Summary of Fs Boost Target K. Defines the boost level for FFE_RES2. NOT in use
sumf_boost_target_c_lane[7:0] | W | Summary of Fs Boost Target C. Defines the boost level for FFE_RES2. NOT in use
DFE_F0_SAT_THRES_LANE[7:0] | W | DFE F0 Saturation Threshold (0~63) => To avoid saturated F0A.
RX_RXFFE_R_INI_LANE[3:0] | W | Rx RXFFE Resistor Initial.
RX_RXFFE_C_INI_LANE[3:0] | W | Rx RXFFE Capacitor Initial.
rxffe_res2_sel_e_g0/1/2/3/4_lane[3:0] | R/W | RXFFE RES2 Select Even For G0-4
rxffe_cap2_sel_e_g0/1/2/3/4_lane[3:0] | R/W | RXFFE CAP2 Select Even For G0-4
rxffe_res2_sel_o_g0/1/2/3/4_lane[3:0] | R/W | RXFFE RES2 Select Odd For G0-4
rxffe_cap2_sel_o_g0/1/2/3/4_lane[3:0] | R/W | RXFFE CAP2 Select Odd For G0-4
rxffe_res1_sel_g0/1/2/3/4_lane[3:0] | R/W | RXFFE RES1 Select Odd For G0-4
rxffe_cap1_sel_g0/1/2/3/4_lane[3:0] | R/W | RXFFE CAP1 Select Odd For G0-4
FFE_DATA_RATE_LANE[3:0] | R/W | FFE Data Rate Selection. Downloaded from the speed table.

## Slide 65: TRAINING – Related Registers
Name of Registers | DIR | Description
ffe_res1_sel_lane[3:0] | R/W | FFE First Stage Resistor Selection. 4'h0: 2.4 dB. 4'h1: 1.5 dB. 4'h2: 0.3 dB. 4'h3: -0.7 dB. 4'h4: -1.7 dB. 4'h5: -2.7 dB. 4'h6: -3.8 dB. 4'h7: -4.6 dB. 4'h8: -5.4 dB. 4'h9: -6.4 dB. 4'hA: -7.5 dB. 4'hB: -8.9 dB. 4'hC: -11.4 dB. 4'hD: -12.6 dB. 4'hE: -15.2 dB. 4'hF: -17.2 dB.
FFE Train – Search Table
Name of Registers | DIR | Description
ffe_cap1_sel_lane[3:0] | R/W | FFE First Stage Capacitor Selection. 4'h0: 2.6 dB. 4'h1: 4.2 dB. 4'h2: 5.2 dB. 4'h3: 6.0 dB. 4'h4: 6.5 dB. 4'h5: 6.9 dB. 4'h6: 7.3 dB. 4'h7: 7.6 dB. 4'h8: 7.8 dB. 4'h9: 8.0 dB. 4'hA: 8.2 dB. 4'hB: 8.5 dB. 4'hC: 8.8 dB. 4'hD: 9.0 dB. 4'hE: 9.2 dB. 4'hF: 9.4 dB.

## Slide 66: TRAINING – Related Registers
Name of Registers | DIR | Description
ffe_res2_sel_o_lane[3:0] | R/W | FFE Second Stage Odd Path Resistor Selection. 4'h0: 4.0 dB. 4'h1: 5.2 dB. 4'h2: 6.2 dB. 4'h3: 7.0 dB. 4'h4: 7.6 dB. 4'h5: 8.2 dB. 4'h6: 8.6 dB. 4'h7: 8.9 dB. 4'h8: 9.2 dB. 4'h9: 9.5 dB. 4'hA: 9.7 dB. 4'hB: 9.9 dB. 4'hC: 10.0 dB. 4'hD: 10.2 dB. 4'hE: 10.3 dB. 4'hF: 10.4 dB.
FFE Train – Search Table
Name of Registers | DIR | Description
ffe_cap2_sel_o_lane[3:0] | R/W | FFE Second Stage Odd Path Cap Selection. 4'h0: 4.0 dB. 4'h1: 5.2 dB. 4'h2: 6.2 dB. 4'h3: 7.0 dB. 4'h4: 7.6 dB. 4'h5: 8.2 dB. 4'h6: 8.6 dB. 4'h7: 8.9 dB. 4'h8: 9.2 dB. 4'h9: 9.5 dB. 4'hA: 9.7 dB. 4'hB: 9.9 dB. 4'hC: 10.0 dB. 4'hD: 10.2 dB. 4'hE: 10.3 dB. 4'hF: 10.4 dB.

## Slide 67: TRAINING – Related Registers
Name of Registers | DIR | Description
ffe_res2_sel_e_lane[3:0] | R/W | FFE Second Stage Even Path Resistor Selection. 4'h0: 4.0 dB. 4'h1: 5.2 dB. 4'h2: 6.2 dB. 4'h3: 7.0 dB. 4'h4: 7.6 dB. 4'h5: 8.2 dB. 4'h6: 8.6 dB. 4'h7: 8.9 dB. 4'h8: 9.2 dB. 4'h9: 9.5 dB. 4'hA: 9.7 dB. 4'hB: 9.9 dB. 4'hC: 10.0 dB. 4'hD: 10.2 dB. 4'hE: 10.3 dB. 4'hF: 10.4 dB.
FFE Train – Search Table
Name of Registers | DIR | Description
ffe_cap2_sel_e_lane[3:0] | R/W | FFE Second Stage Even Path Resistor Selection. 4'h0: 0.4 dB. 4'h1: 0.0 dB. 4'h2: -0.5 dB. 4'h3: -1.5 dB. 4'h4: -2.4 dB. 4'h5: -3.5 dB. 4'h6: -4.6 dB. 4'h7: -5.4 dB. 4'h8: -6.2 dB. 4'h9: -7.3 dB. 4'hA: -8.5 dB. 4'hB: -10.1 dB. 4'hC: -11.9 dB. 4'hD: -14.6 dB. 4'hE: -18.2 dB. 4'hF: -21.2 dB.

## Slide 68: TRAINING – Related Registers
Gain Train – DFE Resolution is a part of Gain Train.
NAME OF REGISTERS | DIR | DESCRIPTION
gain_train_init_en_lane | W | DFE resolution training enable during Tx/Rx train initialize state.
gain_train_end_en_lane | W | DFE resolution training enable during Tx/Rx train end state.
gain_train_with_c_lane | W | FFE capacitor enable during gain train. 1’b0: FFE_CAP will be swept in the search table. 1’b1: FFE_CAP will not be swept in the search table.
rxffe_r_gain_train_lane[3:0] | W | FFE resistor gain train.
gain_train_with_sampler_lane | W | High sensitivity sampler training enable during gain train.
DFE_RES_F0A_HIGH_THRES_INIT_LANE[7:0] | W | DFE resolution F0a high threshold for train initial stage
DFE_RES_F0A_HIGH_THRES_END_LANE[7:0] | W | DFE resolution F0a high threshold for train end stage
DFE_RES_F0A_LOW_THRES_01_INIT_LANE[7:0] | W | DFE resolution F0a low threshold 01 for gain train in train initial stage.
DFE_RES_F0A_LOW_THRES_2_INIT_LANE[7:0] | W | DFE resolution F0a low threshold 2 for gain train in train initial stage.
DFE_RES_F0A_LOW_THRES_3_INIT_LANE[7:0] | W | DFE resolution F0a low threshold 3 for gain train in train initial stage.
DFE_RES_F0A_LOW_THRES_01_END_LANE[7:0] | W | DFE resolution F0a low threshold 01 for gain train in train end stage.
DFE_RES_F0A_LOW_THRES_2_END_LANE[7:0] | W | DFE resolution F0a low threshold 2 for gain train in train end stage.
DFE_RES_F0A_LOW_THRES_3_END_LANE[7:0] | W | DFE resolution F0a low threshold 3 for gain train in train end stage.

## Slide 69: TRAINING – Related Registers
NAME OF REGISTERS | DIR | DESCRIPTION
CFG_RX_EQ_CTRL_LANE | W | PHY Rx training enable while in USB3 LTSSM Polling.RxEQ State, or PCIE LTSSM recovery equalization state. (PIPE lane register) 1'b0: Disable Rx Training. 1'b1: Enable Rx Training.
CFG_UPDATE_POLARITY_LANE | W | Select polarity of coefficient updates at C-1 and C+1. (PIPE lane register) 1'b0: Increment and decrement with signed value. 1'b1: Increment and decrement with absolute value.
cfg_use_ctrl_fld_rst_lane | W | PHY control field reset command select. This bit enables the reset command for remote Tx training. (PIPE lane register) 1'b0: Do not use PHY remote_ctrl_field_reset_lane command. 1'b1: Use phy remote_ctrl_field_reset_lane command.
CFG_CLK_SRC_MASK | W | Clock source mask for master lane to handle lane turn off signaling. (PIPE CMN register) 1'b0: When the lane is the master lane, the lane turn off signal does not disable the whole lane. 1'b1: When the lane is the master lane, the lane off signal enables only the power management block, all other blocks of the lane are disabled.
thre_poor_lane[2:0] | W | DFE level check threshold for poor.
thre_good_lane[4:0] | W | DFE level check threshold for good.
thre_excellent_lane[5:0] | W | DFE level check threshold for excellent.
Others

## Slide 70: TRAINING – Related Registers
Others
NAME OF REGISTERS | DIR | DESCRIPTION
rx_no_init_lane | W | No Rx initial during Rx train. 1’b0: initialize and reset R_INI and C_INI of Rx FFE settings at the beginning of TX/RX training. 1’b1: RX FFE settings are not reset at the beginning of the TX/RX training.
TX_TRAIN_FAILED_LANE | R | Tx Train Failed Status. Rising edge of this bit effective. It is asserted by MCU. It indicates that the local PHY has encountered a problem during training or could not converge.
RX_TRAIN_FAILED_LANE | R | Rx Training Failed Status. This bit is TXCLK domain.
TX_TRAIN_COMPLETE_INT_LANE | R | Tx train complete indicator from MCU.
RX_TRAIN_COMPLETE_LANE | R | Rx Training Complete Status.
TX_TRAIN_ERROR_LANE[1:0] | R | PIN_TX_TRAIN_ERROR read-out register. Latched in when TX_TRAIN_FAILED_LANE = 1. This is only for SAS application.

## Slide 71: COMMAND INTERFACE

## Slide 72: FIRMWARE – COMMAND IF SIGNALS
Signal Name | Dir | Description
PIN_PAPTA_TRAIN_ENABLE | I | PAPTA Transmitter Train Enable
PHY_REMOTE_CTRL_COMMAND_TYPE_LANE[7:0] | I | PHY REMOTE Control Type Command
PHY_REMOTE_CTRL_COMMAND_CODE_LANE[15:0] | I | PHY REMOTE Control Code Command
PHY_REMOTE_CTRL_VALUE_LANE[31:0] | I | PHY REMOTE Control Value
PHY_MCU_REMOTE_REQ_LANE | I | PHY MCU Request
PHY_MCU_LOCAL_ACK_LANE | O | PHY MCU Acknowledge
PHY_LOCAL_STATUS_LANE[7:0] | O | Command Interface Local Status 0: Complete indicator to process current command 1: Invalid indicator for Invalid Command Type or Code
PHY_LOCAL_VALUE_LANE[31:0] | O | PHY Local Value
APTA_TRAIN_SIM_EN | I | APTA Train Simulation Enable 1: Enable APTA train L_A dummy algorithm 0: Normal SOC must set APTA_TRAIN_SIM_EN to 1 before APTA Train start.
APTA_TRAIN_CMD_IF_EN | I | APTA Train Command Interface Simulation Enable 1: Enable APTA Train L_A Command Interface 0: Normal SOC must set APTA_TRAIN_CMD_IF_EN to 1 before APTA Train start.

## Slide 73: FIRMWARE - COMMAND IF SIGNALS
Timing of Command Interface

## Slide 74: FIRMWARE – COMMAND IF SIGNALS
Command Interface Program Sequence
  Set a command by programming PHY_REMOTE_CTRL_COMMAND_TYPE_LANE[7:0], PHY_REMOTE_CTRL_COMMAND_CODE_LANE[15:0], PHY_REMOTE_CTRL_VALUE_LANE[31:0] and PHY_LOCAL_VALUE_LANE[31:0] depending on the interface required.
  Program PHY_MCU_REMOTE_REQ_LANE = 1
  Wait until PHY_MCU_LOCAL_ACK_LANE = 1
  PHY_LOCAL_STATUS_LANE, PHY_LOCAL_VALUE_LANE can be read at this time
  Program PHY_MCU_REMOTE_REQ_LANE = 0
  Wait for PHY_MCU_LOCAL_ACK_LANE = 0 for the next communication
  Repeat above steps.
Firmware Command Tables
  For all commands in the command tables are valid when PHY_REMOTE_CTRL_VALUE_LANE[31] = 1 (in debug state for current speed), direct write and read of PHY hardware registers is possible according to PHY_REMOTE_CTRL_VALUE_LANE[23:0] values for debug purposes, and the PHY_REMOTE_CTRL_VALUE_LANE[27:24] (GEN number) setting is ignored. When new speed values are entered, the register values which had been programmed when PHY_REMOTE_CTRL_VALUE_LANE[31] = 1 are overwritten.

## Slide 75: FIRMWARE – APTA Command Table – For SAS G5 Only
PHY_REMOTE_CTRL_COMMAND_TYPE_LANE[7:0] | PHY_REMOTE_CTRL_COMMAND_CODE_LANE[15:0] | Description
0x60 | 0x0000 | APTA_ADJUST (start)
0x60 | 0x0001 | APTA_COEFFICIENT_1_2 (decrement)
0x60 | 0x0002 | APTA_COEFFICIENT_1_2 (increment)
0x60 | 0x0003 | APTA_COEFFICIENT_2_3 (decrement)
0x60 | 0x0004 | APTA_COEFFICIENT_2_3 (increment)
0x60 | 0x0005 | APTA_COEFFICIENT_2 (decrement)
0x60 | 0x0006 | APTA_COEFFICIENT_2 (increment)
0x60 | 0x0007 | APTA_COEFFICIENT_1 (decrement)
0x60 | 0x0008 | APTA_COEFFICIENT_1 (increment)
0x60 | 0x0009 | APTA_COEFFICIENT_3 (decrement)
0x60 | 0x000A | APTA_COEFFICIENT_3 (increment)
0x60 | 0x000B | APTA_ADJUST (complete)
0x60 | 0x000C | APTA_ADJUST (terminate)

## Slide 76: FIRMWARE - APTA Command Table
APTA_TRAIN_CMD_IF_EN Setting
  Note: For the APTA command selection, PIN_PAPTA_TRAIN_ENABLE and APTA_TRAIN_CMD_IF_EN must each be 0x1, before asserting PIN_PAPTA_TRAIN_ENABLE.
Signal Name | Dir | Description
APTA_TRAIN_CMD_IF_EN | I | APTA Train Command Interface Simulation Enable. 0: Normal mode. 1: Enable APTA train all commands interface. This bit need be set to 1 before APTA train start. When this bit is 1, PIN_LOCAL_CTRL_FIELD_RESET[3:0] and PIN_LOCAL_CTRL_FIELD[5:0] are used for APTA Train

## Slide 77: FIRMWARE – Tx Command Table (1)
COMMAND_TYPE_LANE[7:0] | PHY_REMOTE_CTRL_COMMAND_CODE_LANE[15:0] | PHY_REMOTE_CTRL_VALUE_LANE[31:0] | PHY_LOCAL_VALUE_LANE[31:0] | Description
0x80 | 0x0000 | [31]: Debug for current speed [27:24]: GEN number [15:12]: Peak emphasis control [11:8]: Pre emphasis control [7:4]: Post emphasis control [3]: Enable peak emphasis control [2]: Enable pre emphasis control [1]: Enable post emphasis control [0]: Force TXFFE control Enable 0: Enable adapted value during training 1; Force to stay on user program value from command interface during training | None | Set Tx FFE control per GEN
0x80 | 0x0001 | [31]: Debug for current speed [27:24]: GEN number | [31]: Debug for current speed [27:24]: GEN number [15:12]: Peak emphasis control [11:8]: Pre emphasis control [7:4]: Post emphasis control [3]: Enable peak emphasis control [2]: Enable pre emphasis control [1]: Enable post emphasis control [0]: Force TXFFE control Enable | Get Tx FFE control per GEN

## Slide 78: FIRMWARE – Tx Command Table (2)
COMMAND_TYPE_LANE[7:0] | PHY_REMOTE_CTRL_COMMAND_CODE_LANE[15:0] | PHY_REMOTE_CTRL_VALUE_LANE[31:0] | PHY_LOCAL_VALUE_LANE[31:0] | Description
80 | 0x0006 | [31]: Debug for current speed [27:24]: GEN number [17:16]: Slew rate enable 2b00: Fast slew rate 2b11: Slow slew rate Others: Not valid [9:8]: Slew control 1 [1:0]: Slew control 0 | None | Set Tx slew rate per GEN
0x80 | 0x0007 | [31]: Debug for current speed [27:24]: GEN number | [31]: Debug for current speed [27:24]: GEN number [17:16]: Slew rate enable 2b00: Fast slew rate 2b11: Slow slew rate Others: Not valid [9:8]: Slew control 1 [1:0]: Slew control 0 | Get Tx slew rate per GEN

## Slide 79: FIRMWARE – Tx Command Table (3)
COMMAND_TYPE_LANE[7:0] | PHY_REMOTE_CTRL_COMMAND_CODE_LANE[15:0] | PHY_REMOTE_CTRL_VALUE_LANE[31:0] | PHY_LOCAL_VALUE_LANE[31:0] | Description
0x80 | 0x0008 | [31]: Debug for current speed [27:24]: GEN number [16]: SSC enable [8]: SSC down/center spread select 0: Center-spread 1: Down-spread [6:0]: SSC amplitude | None | Set Tx SSC control per GEN
0x80 | 0x0009 | [31]: Debug for current speed [27:24]: GEN number | [31]: Debug for current speed [27:24]: GEN number [16]: SSC enable [8]: SSC down/center spread select 0: Center-spread 1: Down-spread [6:0]: SSC amplitude | Get Tx SSC control per GEN
0x80 | 0x000A | [2:0]: Tx margin | None | Set Tx margin
0x80 | 0x000B | None | [2:0]: Tx margin | Get Tx margin

## Slide 80: FIRMWARE – Tx Command Table (4)
COMMAND_TYPE_LANE[7:0] | PHY_REMOTE_CTRL_COMMAND_CODE_LANE[15:0] | PHY_REMOTE_CTRL_VALUE_LANE[31:0] | PHY_LOCAL_VALUE_LANE[31:0] | Description
0x81 | 0x0000 | [7:0]: Local Tx preset index In SAS mode 0: Not used 1: Reference 1 2: Reference 2 3: No equalization In SerDes mode 4: Initial 5: Preset The others PHY mode is not applicable | None | Set Tx preset index
0x81 | 0x0001 | None | [7:0]: Local Tx preset index | Get Tx preset index
0x81 | 0x0002 | [31]: Debug for current speed [27:24]: Tx preset table selection [21:16]: Peak emphasis [13:8]: Pre emphasis [5:0]: Post emphasis | None | Set Tx preset table

## Slide 81: FIRMWARE – Tx Command Table (5)
COMMAND_TYPE_LANE[7:0] | PHY_REMOTE_CTRL_COMMAND_CODE_LANE[15:0] | PHY_REMOTE_CTRL_VALUE_LANE[31:0] | PHY_LOCAL_VALUE_LANE[31:0] | Description
0x81 | 0x0003 | [27:24]: Tx preset table selection In SAS mode 0: Not used 1: Reference 1 2: Reference 2 3: No equalization In SerDes mode 4: Initial 5: Preset The others PHY mode is not applicable | [27:24]: Tx preset table selection [21:16]: Peak emphasis [13:8]: Pre emphasis [5:0]: Post emphasis | Get Tx preset table

## Slide 82: FIRMWARE – Rx Command Table (1)
PHY_REMOTE_CTRL_COMMAND_TYPE_LANE[7:0] | PHY_REMOTE_CTRL_COMMAND_CODE_LANE[15:0] | PHY_REMOTE_CTRL_VALUE_LANE[31:0] | PHY_LOCAL_VALUE_LANE[31:0] | Description
0x82 | 0x0000 | [31]: Debug for current speed [27:24]: GEN number [15:12]: Phase loop final coefficient [11:8]: Phase loop initial coefficient [6:4]: Final multiple frequency selection [2:0]: Initial multiple frequency selection | None | Get Rx CDR BW per GEN.
0x82 | 0x0001 | [31]: Debug for current speed. [27:24]: GEN number | [31]: Debug for current speed [27:24]: GEN number [15:12]: Phase loop final coefficient [11:8]: Phase loop initial coefficient [6:4]: Final multiple frequency selection [2:0]: Initial multiple frequency selection | Get Rx CDR BW per GEN.

## Slide 83: FIRMWARE – Rx Command Table (2)
PHY_REMOTE_CTRL_COMMAND_TYPE_LANE[7:0] | PHY_REMOTE_CTRL_COMMAND_CODE_LANE[15:0] | PHY_REMOTE_CTRL_VALUE_LANE[31:0] | PHY_LOCAL_VALUE_LANE[31:0] | Description
0x82 | 0x0002 | [31]: Debug for current speed [27:24]: GEN number [23:20]: FFE 2nd stage odd resistor selection [19:16]: FFE 2nd stage odd capacitor selection [15:8]: Reserved [7:4]: FFE 1st stage resistor selection [3:0]: FFE 1st stage capacitor selection | None | Set Rx FFE resistor and capacitor selection per GEN.
0x82 | 0x0003 | [31]: Debug for current speed [27:24]: GEN number | [31]: Debug for current speed [27:24]: GEN number [23:20]: FFE 2nd stage odd resistor selection [19:16]: FFE 2nd stage odd capacitor selection [15:8]: Reserved [7:4]: FFE 1st stage resistor selection [3:0]: FFE 1st stage capacitor selection | Get Rx FFE resistor and capacitor selection per

## Slide 84: FIRMWARE – Rx Command Table (3)
PHY_REMOTE_CTRL_COMMAND_TYPE_LANE[7:0] | PHY_REMOTE_CTRL_COMMAND_CODE_LANE[15:0] | PHY_REMOTE_CTRL_VALUE_LANE[31:0] | PHY_LOCAL_VALUE_LANE[31:0] | Description
0x82 | 0x0004 | [31]: Debug for current speed. [27:24]: GEN number [9]: DFE enable selection 0: From PIN_DFE_EN 1: From command interface [8]: DFE enable [7]: F5, F6 and F7 resolution [6]: F8 to F15 resolution [5]: Floating tap resolution [4:3]: F0 resolution [2:1]: F1 resolution [0]: F2, F3 and F4 resolution | None | Set Rx DFE enable and resolution per GEN.

## Slide 85: FIRMWARE – Rx Command Table (4)
PHY_REMOTE_CTRL_COMMAND_TYPE_LANE[7:0] | PHY_REMOTE_CTRL_COMMAND_CODE_LANE[15:0] | PHY_REMOTE_CTRL_VALUE_LANE[31:0] | PHY_LOCAL_VALUE_LANE[31:0] | Description
0x82 | 0x0005 | [31]: Debug for current speed. [27:24]: GEN number | [31]: Debug for current speed [27:24]: GEN number [9]: DFE enable selection 0: From PIN_DFE_EN 1: From command interface [8]: DFE enable [7]: F5, F6 and F7 resolution [6]: F8 to F15 resolution [5]: Floating tap resolution [4:3]: F0 resolution [2:1]: F1 resolution [0]: F2, F3 and F4 resolution | Get Rx DFE enable and resolution per GEN.

## Slide 86: FIRMWARE – Calibration Command Table (1)
PHY_REMOTE_CTRL_COMMAND_TYPE_LANE[7:0] | PHY_REMOTE_CTRL_COMMAND_CODE_LANE[15:0] | PHY_REMOTE_CTRL_VALUE_LANE[31:0] | PHY_LOCAL_VALUE_LANE[31:0] | Description
0x82 | 0x0006 | [31]: Debug for current speed. [27:24]: GEN number [4:0]: Squelch detector threshold ratio | None The squelch threshold = (SQ threshold calibration result) * ratio When SQ threshold ratio != 0, the ratio = (SQ threshold ratio) / 32 When SQ threshold ratio = 0, the ratio = 1 Note, SQ threshold ratio is user defined by SQ detector threshold ratio | Set SQ threshold ratio per GEN.
0x82 | 0x0007 | [31]: Debug for current speed. [27:24]: GEN number | [31]: Debug for current speed [27:24]: GEN number [4:0]: SQ detector threshold ratio | Get SQ threshold ratio per GEN.
0x83 | 0x0000 | [0]: Bypass CTLE train | None | Set bypass CTLE train.
0x83 | 0x0001 | None | [0]: Bypass CTLE train | Get bypass CTLE train.

## Slide 87: FIRMWARE – Calibration Command Table (2)
PHY_REMOTE_CTRL_COMMAND_TYPE_LANE[7:0] | PHY_REMOTE_CTRL_COMMAND_CODE_LANE[15:0] | PHY_REMOTE_CTRL_VALUE_LANE[31:0] | PHY_LOCAL_VALUE_LANE[31:0] | Description
0x84 | 0x0000 | [0]: Lane selection 0: lane0 1: lane1 Both lanes cannot be executed for hardware limitation. | Rx impedance calibration | Run Rx impedance calibration
0x84 | 0x0001 | [0]: Lane selection 0: lane0 1: lane1 Both lanes cannot be executed for hardware limitation. | Tx impedance calibration | Run Tx impedance calibration